Place , date ……………………………..

Supplier filing a declaration:

………………………………………….

(Name , if possible stamp of a supplier)

|  | Ordering party: GP ECO SPÓŁKA Z OGRANICZONĄ ODPOWIEDZIALNOŚCIĄ 4 Stalowa, 47-400 Racibórz |
| --- | --- |

Appendix No.1: Quotation form.

With regards to the quotation inquiry No. 04/POIR.03.02.02-00-1283/17 dated 13.06.2017, about the purchase of a fixed asset – Induction Furnace, we, hereby, present our offer:

| Induction Furnace | Unit parameters and equipment – detailed description | Net price |
| --- | --- | --- |
|  | Induction furnace will be used for melting aluminium in pieces, chips and combined with steel. Inside it, there will be produced an alloy of aluminum with the alloying required for innovative alloys (Silumin) in the form of elements or pre-alloys. SPECIFICATION: Capacity: 2 750 kg, Furnace power: 800 kW, Nominal frequency at a completely filled ,with liquid metal, furnace: 150 Hz, Clear Diameter of cone crucible: 940 mm, Clear depth of the crucible: 1980 mm, Melting efficiency: - at furnace maximum power rating – pieces: 1250 kg - at furnace maximum power rating – chips: 1 000 kg, CE Declaration and mark, PLC with 17-19 inch display, Scaling system, Lid with ventilation system, Crucible feeding system, Cooling system with plate exchanger, Temperature controlling system. Electric supply: Power grid: upto 20 000 V Three chase current: 50 Hz TRANSFORMER: Capacity: 950 kVA HYDRAULIC SYSTEM: Time of tilting when emptying furnace: 65s Oil capacity: 210 litres Motor rated load capacity: 180 kW Operating pressure of the hydraulic system: 24 bar Valves’s voltage: 24 V COOLING SYSTEM: Cooling output: 460 kW Protection against frost: min – 25oC Noise level within 15 m range acc.to EN 13487 cooling tower 72 dB (A) | Net price …………………………………………… (in words …………………………………………………………………………… |

Any words used to describe the Subject of the Order, which may indicate a particular manufacturer / supplier, is used solely and exclusively to determine minimum technical requirements that the Ordering Party is expecting with regards to the Order Object.

Delivery Date: …………………………………………………….

Warranty terms: ………………………………………………..

We declare that we have been aware of the terms of the quotation inquiry, we do not raise any objections and we consider ourselves to be bound by its terms.

Supplier’s details:

Contact person …………………………………………………………………..

Tel.: ………………………………………………………………………………………….

e-mail: ……………………………………………………………………………

………………………………………………………

Date and signature (including a stamp if available) of the supplier’s representative

(supplier’s stamp)